## Slide 1
SNMP adaptor to BDS data
Stefan Lieberth
stefan@rtbrick.com
+49 160 90919244

## Slide 2
SNMP agent for RtBrick Systems
  utilizing the loopback-If (IPv4 and IPv6) from Rtbrick Container.
  Supported Versions: v2c and v3
  All SNMP methods must be supported:
    Snmp get,
    Snmp get-next,
    Snmp get-bulk
    Snmp trap + ( inform – if required )
Goals of SNMP Adaptor Framework
collocated on RtBRick Container
  Requires RtBrickContainer to run on 18.4
  Deployment OS will be Ubuntu 18.4
  Main SW elements:
    python 3.6 (for aiohttp REST server)
    Pysnmp 4.4.8
  Performance goals.
    Up to 10k managed Oids (mainly testing effort)
    Up to 50 traps per second
  BDS table data is pushed from RtBrick cont.
    Push trigger needs attention:
      If-status-change triggers push
      If-counter change does not trigger push
  Traps will be send immediately

## Slide 3
l2-pod2 - 5916 - ONL
Snmp lxc container. 10.0.3.20
rtbrick lxc 10.0.3.10
SNMP Server
bdsSnmpRetrieveAdapter.py
bdsSnmpTrapAdapter.py
REST
Request POST push Logging Data
bdsAccess
snmpEngine
bdsData
oidDB
MappingFunc
(per bdsTable)
MappingFunc
(per bdsTable)
restServer
logDataQueue
SnmpTrapGenerator
with embedded mapping function
Snmp Front-End
lookups
update
High Level Overview demo environment
lookups
SNMPv2c
Ntrap.notif.
SNMP v3
Get/getNext
REST
Request POST BDS Table
192.168.202.126
Iptables nat
192.168.202.126
Iptables nat

## Slide 4
Chassis with ONL
LXC: RtBrick Ubuntu 18.4
SNMP Server A
bdsSnmpRetrieveAdapter.py
bdsSnmpTrapAdapter.py
bdsAccess
snmpEngine
oidDB
MappingFunc
(per bdsTable)
MappingFunc
(per bdsTable)
restServer
SnmpTrapGenerator
with embedded mapping function
snmp Front-End
lookups
update
Deployment High Level Overview
lookups
Rtbrick processes
REST Server
Python shared-list
logDataQueue
REST
Request POST push BDS data
REST
Request POST ( binary SNMP packet data)
JSON
restClient
SNMP Server B
SNMP v3
Get/getNext
response.
SNMPv2c
trap.notif.
SNMP v3
Get/getNext
response.
SNMPv2c
trap.notif.
UDP
NAT relay
based on
VPP/DPDK
SNMP v3 Get/getNext
responses
SNMPv2c trap.notif.
Socket(UDP 161)
Server-mode
Socket(UDP)
Client-mode
ubuntu
lo0
ubuntu
lo0
Dest NAT lo1->lo0 (for dest-port 161)
Src NAT lo0 -> lo1 (for src-port 161)
Src NAT lo0 -> lo1 (for dst-port 162)
BDS Table(s) for SNMP configuration
IP endpoints of Servers
V2c options
V3 options
Snmp cfg params
(Rtb) lo1
Snmp cfg params

## Slide 5
bdsSnmpRetrieveAdaptor.py
bdsAccess
snmpEngine MibInstrumController
Retrieve data transcoding example
{
"table": {
"table_name": "global.startup.status.confd"
},
"objects": [
{
"sequence": 5,
"update": true,
"attribute": {
"module_name": "bd",
"startup_status": "02",
"up_time": "19482b5c642e696e",
"bd_name": "confd"
}
}
}
}
staticAndPredefinedOids.py
mappingFuncModule (per bds table)
mappingFuncModule (per bds table)
dynamic data
static data
oidDb
Snmp Front-End
CommunityData
UdpTransportTarget,
ContextData
self.firstItem = None
self.oidDict = {}. #Key = oid; value = oidItem
self.lock = False
oidItem
oid : oidString (dotted)
name : (from MIB)
pysnmp type : (refers to pysnmp
value : mib value
nextOid : oidItem
oidItem
oid : oidString (dotted)
name : (from MIB)
pysnmp type : (refers to pysnmp
value : mib value
nextOid : oidItem
oidItem
oid : oidString (dotted)
name : (from MIB)
pysnmp type : (refers to pysnmp
value : mib value
nextOid : oidItem
class oidItem
Sorted (linked) objects
insertOid()
covers also update
Lock ()
Do wee need this
deleteOidsWithPrefix () used to delete tables
readVars()
Await unlock state
readNextVars()
Await unlock state
oidSegment = "1.3.6.1.4.1.50058.101.3.1."
indexString = bdsJsonObject["attribute"]["module_name"]
indexCharList = [str(ord(c)) for c in indexString]
index = str(len(indexCharList)) + "." + ".".join(indexCharList)
targetOidDb.insertOid(newOidItem = OidDbItem(
oid = oidSegment+"1."+str(index),
name="moduleName",
pysnmpBaseType="OctetString",
value=indexString))
….
targetOidDb.insertOid(newOidItem = OidDbItem(
oid = oidSegment+"4."+str(index),
name="upTime", pysnmpBaseType="OctetString",
value=bdsJsonObject["attribute"]["startup_status"]))
SNMPv2-SMI::enterprises.50058.101.3.1.1.2.98.100 = STRING: "bd"
SNMPv2-SMI::enterprises.50058.101.3.1.1.3.98.100.115 = STRING: "bds"
SNMPv2-SMI::enterprises.50058.101.3.1.1.4.108.119.105.112 = STRING: "lwip"
SNMPv2-SMI::enterprises.50058.101.3.1.2.2.98.100 = STRING: "confd"
SNMPv2-SMI::enterprises.50058.101.3.1.2.3.98.100.115 = STRING: "confd"
SNMPv2-SMI::enterprises.50058.101.3.1.2.4.108.119.105.112 = STRING: "confd"
SNMPv2-SMI::enterprises.50058.101.3.1.3.2.98.100 = STRING: "9fec415c642e696e"
SNMPv2-SMI::enterprises.50058.101.3.1.3.3.98.100.115 = STRING: "9fec415c2e696e63"
SNMPv2-SMI::enterprises.50058.101.3.1.3.4.108.119.105.112 = STRING: "9fec415c2e707562"
SNMPv2-SMI::enterprises.50058.101.3.1.4.2.98.100 = STRING: "02"
SNMPv2-SMI::enterprises.50058.101.3.1.4.3.98.100.115 = STRING: "02"
SNMPv2-SMI::enterprises.50058.101.3.1.4.4.108.119.105.112 = STRING: "02"
REST
Request POST BDS Table
Response POST BDS Table JSON
Response
SNMP
Get/GetNext
Change to push modelL

## Slide 6
Requirements
Human Readable Name | Model Name | Source Organization | Management Protocol | Requirement | Phase | Notes
SNMP | SNMP-FRAMEWORK-MIB | SNMPv3 Working Group | SNMP | MUST | PoC | Especially snmpEngineID, snmpEngineBoots, snmpEngineTime
System | SNMPv2-MIB | IETF SNMPv3 Working Group | SNMP | MUST | PoC | Especially: sysName, sysDescr, sysObjectID, sysUptime, sysContact, sysLocation, sysServices
Interfaces | IF-MIB | IETF Interfaces MIB Working Group | SNMP | MUST | PoC | Especially: ifTableLastChange, ifStackLastChange, ifnumber, ifTable, ifXTable, ifStackTable, ifRcvAddressTable
Entities | ENTITY-MIB | IETF Energy Management Working Group | SNMP | MUST | PoC | Especially: entPhysicalTable, entLogicalTable, entLastChangeTime
LLDP | LLDP-MIB | IEEE 802.1 Working Group | SNMP | MUST | EFT | 
LLDP | LLDP-V2-MIB | IEEE 802.1 Working Group | SNMP | MUST | EFT | Especially: lldpV2LocPortTable
IP | IP-MIB | IETF IPv6 MIB Revision Team | SNMP | MUST | EFT | Especially: ipAddrTable, ipAddressTable
Ethernet | EtherLike-MIB | IETF Ethernet Interfaces and Hub MIB Working Group | SNMP | OPTIONAL | PostEFT | Especially: dot3StatsTable

## Slide 7
bdsLoggingToSnmpNotification.py
Transcoding example for notification RTBRICK-SYSLOG-MIB
RtBrick LXC
SNMP Server
Class asyncioTrapGenerator
Snmp trap
REST Client
class asyncioRestServer
REST Request
RTBRICK-SYSLOG-MIB
Rest Server
( „sysUpTime“ ),
( ntforg.MibVariable('RTBRICK-SYSLOG-MIB', 'syslogMsgNumber', 0), y ),
( ntforg.MibVariable('RTBRICK-SYSLOG-MIB', 'syslogMsgFacility', 0), x ),
( ntforg.MibVariable('RTBRICK-SYSLOG-MIB', 'syslogMsgSeverity', 0), x ),
( ntforg.MibVariable('RTBRICK-SYSLOG-MIB', 'syslogMsgText', 0), x),
{"host":"confd",
"level":3,
"full_message":"",
"short_message":"",
"_time_stamp":"6637363453315326292",
"_rtbrick_host":"Basesim",
"_rtbrick_pod":"rtbrick-pod"}
Set by redisToSnmpTrap.py
Frame 14027: 207 bytes on wire (1656 bits), 207 bytes captured (1656 bits) on interface 0
Null/Loopback
Internet Protocol Version 4, Src: 127.0.0.1, Dst: 127.0.0.1
User Datagram Protocol, Src Port: 64271, Dst Port: 162
Simple Network Management Protocol
version: v2c (1)
community: public
data: snmpV2-trap (7)
snmpV2-trap
request-id: 4518818
error-status: noError (0)
error-index: 0
variable-bindings: 6 items
SNMPv2-MIB::sysUpTime.0 (1.3.6.1.2.1.1.3.0): 11363
SNMPv2-MIB::snmpTrapOID.0 (1.3.6.1.6.3.1.1.4.1.0): 1.3.6.1.4.1.50058.3.1.0.1 (RTBRICK-SYSLOG-MIB::rtbrickSyslogTrap)
RTBRICK-SYSLOG-MIB::syslogMsgNumber.0 (1.3.6.1.4.1.50058.2.1.1.1.0): 4
RTBRICK-SYSLOG-MIB::syslogMsgFacility.0 (1.3.6.1.4.1.50058.2.1.1.2.0): confd
RTBRICK-SYSLOG-MIB::syslogMsgSeverity.0 (1.3.6.1.4.1.50058.2.1.1.3.0): critical (3)
RTBRICK-SYSLOG-MIB::syslogMsgText.0 (1.3.6.1.4.1.50058.2.1.1.4.0): full_message_text
curl -X POST -H "Content-Type: application/json" -H "Accept: */*" -v -H "connection: close"\
-H "Accept-Encoding: application/json"\
-d '{"host":"confd","full_message":"full_message_text","short_message":"short_message_text", "level":3,"_time_stamp":"6637363453315326292","_rtbrick_host":"Basesim","_rtbrick_pod":"rtbrick-pod"}'\
"http://192.168.56.1:5000/anyurl"
Wireshark decode
Curl
Test
message
Periodic attempts to retrieve of list elements
v2c / v3
Trap Generator
Transcoding logic from BDS JSON to SNMP oid
logData
(list)

## Slide 8
notificator.py
Transcoding example for notification RTBRICK-SYSLOG-MIB
SNMP Server
Class AsyncioTrapGenerator
Snmp trap
graylogTestClient.py
class AsyncioRestServer
REST Request
RTBRICK-SYSLOG-MIB
Rest Server
Simple Network Management Protocol
version: v2c (1)
community: public
data: snmpV2-trap (7)
snmpV2-trap
request-id: 11172467
error-status: noError (0)
error-index: 0
variable-bindings: 6 items
SNMPv2-MIB::sysUpTime.0 (1.3.6.1.2.1.1.3.0): 0
SNMPv2-MIB::snmpTrapOID.0 (1.3.6.1.6.3.1.1.4.1.0): 1.3.6.1.4.1.50058.103.1.1 (RTBRICK-MIB::rtbrickSyslogNotifications.1)
RTBRICK-SYSLOG-MIB::syslogMsgNumber.0 (1.3.6.1.4.1.50058.104.2.1.1.0): 1
RTBRICK-SYSLOG-MIB::syslogMsgFacility.0 (1.3.6.1.4.1.50058.104.2.1.2.0): stefans-Air-2.fritz.box
RTBRICK-SYSLOG-MIB::syslogMsgSeverity.0 (1.3.6.1.4.1.50058.104.2.1.3.0): notice (6)
RTBRICK-SYSLOG-MIB::syslogMsgText.0 (1.3.6.1.4.1.50058.104.2.1.4.0): hello gelf
Wireshark decode
graylog
Test
message
Periodic attempts to retrieve of list elements
v2c / v3
Trap Generator
Transcoding logic from BDS JSON to SNMP oid
logData
(list)
$ python3 graylogTestClient.py
POST /gelf HTTP/1.1
Host: 127.0.0.1:5000
Accept-Encoding: identity
Content-Length: 119
{"version":"1.1",
"short_message":"hello gelf", "timestamp":1553302278.198669,
"level":6,
"host":"stefans-Air-2.fritz.box"}

## Slide 9
notificator.py
Rtbrick logging to bdsSnmpAdaptor config
SNMP Server
Class AsyncioTrapGenerator
Snmp trap
graylogTestClient.py
class AsyncioRestServer
REST Request
RTBRICK-SYSLOG-MIB
Rest Server
rtb confd set snmp server-ip 10.0.3.20 server-port 5000 server-ep test-end bd-name fwdd.hald
rtb confd set log module fwd logmap FWDD_IFP_ADMIN_STATUS level info plugin-type snmp bd-name fwdd.hald
rtb confd set log module fwd logmap FWDD_IFL_ADMIN_STATUS level info plugin-type snmp bd-name fwdd.hald
rtb confd set log module fwd logmap FWDD_IFP_LINK_STATUS level info plugin-type snmp bd-name fwdd.hald
rtb confd set log module fwd logmap FWDD_IFL_LINK_STATUS level info plugin-type snmp bd-name fwdd.hald
rtb fwdd.hald show log enabled status
rtb confd set interface physical ifp-0/0/35 disable
rtb confd delete interface physical ifp-0/0/35 disable
Wireshark decode
Periodic attempts to retrieve of list elements
v2c / v3
Trap Generator
Transcoding logic from BDS JSON to SNMP oid
logData
(list)

## Slide 10
bdsSnmpAdaptor
  concept for datagram-passthrough to pysnmp snmpEngine
  Integrate / Consider MIBs from Jan
  Add entity-MIB to OID-mapping
Next steps / Todos / Risks
Rtbrick container
  Ubuntu 18.4 support
  Passthrough of snmp datagrams via VPP NAT table
  BDS push modell with configurable triggers (table Object attribute change)
  Interfaces counters for logical interfaces
Integration
  Get access to spectrum system and study requirements
  Test integration with bdsSnmpAdaptor

## Slide 11
Example 5916 - Entity MIB Hierarchy
iso.3.6.1.2.1.47.1.1.1.1.2 |  |  |  | 
index | Description | Contained in | is FRU | Serial
1 | Rtbrick Fullstack Chasses | 0 | yes | 591654XK1848008
2 | Switch Module Container | 1 | no | if available
3 | CPU Module Container | 1 | no | if available
4 | Power Supply Container | 1 | yes | if available
5 | Power Supply Container | 1 | yes | if available
6 | Fan Container | 1 | yes | if available
7 | Fan Container | 1 | yes | if available
8 | Fan Container | 1 | yes | if available
9 | Fan Container | 1 | yes | if available
10 | Fan Container | 1 | yes | if available
11 | Fan Container | 1 | yes | if available
12 | Management Ethernet Port | 3 | no | -
13 | USB Port | 3 | no | -
14 | Console Port | 3 | no | -
15 | SFP Container Port 1 | 2 | no | -
16 | SFP Container Port 2 | 2 | no | -
61 | SFP Container Port 47 | 2 | no | -
62 | SFP Container Port 48 | 2 | no | -
63 | XSFP Container Port 49 | 2 | no | -
68 | XSFP Container Port 54 | 2 | no | -
69 | SFP-10G-DAC | 15 | yes | F1712078x01
70 | SFP-10G-DAC | 16 | yes | F1712078x02
71 | SFP-10G-DAC | 17 | yes | F1712078x03
72 | SFP-10G-DAC | 18 | yes | F1712078x04
73 |  | 19 | yes | 
76 |  | 22 | yes | 
77 | QSFP-4SFP10G-DAC | 23 | yes | F1712078x09
78 | QSFP-4SFP10G-DAC | 24 | yes | F1712078x10
79 | QSFP-4SFP10G-DAC | 25 | yes | F1712078x11
80 | QSFP-4SFP10G-DAC | 26 | yes | F1712078x12
81 |  | 27 | yes | 
117 | Q28-PC03 | 63 | yes | F1712078x49
118 | Q28-PC04 | 64 | yes | F1712078x50
119 |  | 65 | yes | 

## Slide 12
Example 5916 - show chassis hardware/environment (or similar)

## Slide 13
Example 5916 - show chassis hardware/environment (or similar)

## Slide 14
Next steps / Todos / Risks
Risk Event | # | Timeframe | Probability | Risk mitigation plan
UDP Passthrough via VPP NAT is not available in time | 1 | 31.3.2019 | 50% | Probably showstopper
Availability of Entitiy Mib data. It is required that RtBrick implements table and data-import from ONL linux | 2 | 31.3.2019 | 50% | Ongoing tracking with engineering
Availability of status change attributes for IF-table and IF-Table objects. | 3 | 20.3.2019 | 0% | Solved,
Logging import via Rest and define logging MIB | 4 | 15.3.2019 | 30% | Rtb documentation required
Available of Push model for BDS table, incl push triggers configuration | 5 | 15.4.2019 | 50% | 
Implement Required MIBs for v3 USM support Implement SNMP-FRAMEWORK-MIB | 6 | 20.3.2019 | 10% | Almost done, just tests needed
hrSystemUptime info Rtbrick -> snmpAdaptor | 7 | 31.3.2019 | 20% | 
Time Sync trap> retrieve – combine two modules to one | 8 | 31.3.2019 | 20% | 
unforeseen circumstance during Early Field Trial | 9 | 31.5.2019 | 40% | 

## Slide 15
Next steps / Todos / Risks
Risk Event | # | Timeframe | Probability | Risk mitigation plan | rtbrick debendency -> bug id
UDP Passthrough via VPP NAT is not available in time | 1 | 31.03.19 | 50% | Probably showstopper | 1025
Availability of Entitiy Mib data. It is required that RtBrick implements table and data-import from ONL linux | 2 | 31.03.19 | 50% | Ongoing tracking with navaneeth | 1053
Availability of status change attributes for IF-table and IF-Table objects. | 3 | 20.03.19 | 0% | Solved, | 
Logging import via Rest and define logging MIB | 4 | 31.03.19 | 30% | Rtb documentation required | 1326, 1238, 1351
Available of Push model for BDS table, incl push triggers configuration | 5 | 15.04.19 | 50% |  | ?
Implement Required MIBs for v3 USM support | 6 | 20.03.19 | 0% | Almost done, just tests needed | 
Implement SNMP-FRAMEWORK-MIB |  |  |  |  | 
hrSystemUptime info Rtbrick -> snmpAdaptor | 7 | 31.3.2019 | 20% |  | 
Time Sync notifier <-> responder – combine two modules to one | 8 | 31.03.19 | 20% |  | 
unforeseen circumstance during Early Field Trial | 9 | 31.05.19 | 40% |  | 

## Slide 16
SNMP walk Example.
stefans-Air:bdsSnmpAdaptor sli$ snmpwalk -v 2c -c public -m ALL -M /Users/Shared/snmp/mibs 192.168.202.126 1.3.6 2> /dev/null
SNMPv2-SMI::mib-2.1.1.0 = STRING: "sysDesc123"
SNMPv2-SMI::mib-2.1.2.0 = OID: RTBRICK-MIB::rtbrick
SNMPv2-SMI::mib-2.1.3.0 = Timeticks: (3055258) 8:29:12.58
SNMPv2-SMI::mib-2.1.4.0 = STRING: "sysContact123@example.com"
SNMPv2-SMI::mib-2.1.5.0 = STRING: "sysName123"
SNMPv2-SMI::mib-2.1.6.0 = STRING: "sysLocation123"
SNMPv2-SMI::mib-2.1.7.0 = INTEGER: 6
IF-MIB::ifInOctets.4096 = Counter32: 0
IF-MIB::ifInOctets.8192 = Counter32: 0
IF-MIB::ifInOctets.12288 = Counter32: 0
IF-MIB::ifInOctets.16384 = Counter32: 0
stefans-Air:runbookGenerator sli$ snmpwalk -v 3 -n "" -u testUser2 -a SHA -A "authKey123" -l authNoPriv 192.168.202.126 1.3.6 2> /dev/null
SNMPv2-MIB::sysDescr.0 = STRING: bdsSnmpAdaptor v0.5.2
SNMPv2-MIB::sysObjectID.0 = OID: SNMPv2-SMI::enterprises.50058
DISMAN-EVENT-MIB::sysUpTimeInstance = Timeticks: (7329) 0:01:13.29
SNMPv2-MIB::sysContact.0 = STRING: sysContact123@example.com
SNMPv2-MIB::sysName.0 = STRING: sysName123
SNMPv2-MIB::sysLocation.0 = STRING: sysLocation123
SNMPv2-MIB::sysServices.0 = INTEGER: 6
SNMPv2-SMI::zeroDotZero = No more variables left in this MIB View (It is past the end of the MIB tree)

## Slide 17
L2-POD2 - 5916 – ONL 192.168.202.126
Snmp lxc container. 10.0.3.20
RtBrick lxc 10.0.3.10
responder.py
REST
Request POST
testExecutor (on Mac OS)
iptables NAT forwarding
responses
SNMP v2c
SNMP v3
RtBrick fwdd-hald process
48 + 6 physical ports
BDS
Spectrum
SNMP Server
SSH
SSH
SNMP v2c
SNMP v3