## Slide 1
SNMP adaptor to BDS data
Stefan Lieberth
stefan@rtbrick.com
+49 160 90919244

## Slide 2
Goals of SNMP Adaptor
PoC Architectur / Data-Structures / test-Bed
Deployment Architecture
Agenda

## Slide 3
SNMP agent for RtBrick Systems
  Supported Versions: v2c and v3
  All SNMP methods must be supported:
    Snmp get,
    Snmp get-next,
    Snmp get-bulk
    Snmp trap / inform
  Utilizing pysnmp library
Goals of SNMP Adaptor

## Slide 4
PoC Architecture (pull to BDS via REST POST)
Linux Hosts
RtBrick LXC
SNMP Server
bdsSnmpAtaptor.py
(pysnmp) MibInstrumController
bdsTablesToRedis
SNMP Requests
get, getnext getbuld
Snmp Response
redisToSnmpTrap.py
Snmp trap
REST Client
restServerFor-RtBrickSnmp-TrapsToRedis.py
REST Request
{"host":"confd",
"full_message":"",
"short_message":"",
"level":3,
"_time_stamp":"6637363453315326292",
"_rtbrick_host":"Basesim",
"_rtbrick_pod":"rtbrick-pod"}
REST Server
BS databse
Redis DB for
Cache / Queue
(bdsSnmpTables..py)
Periodic
Or
Triggered
Oid Table Refresh
htpp request
http Response
RTBRICK-SYSLOG-MIB
Key/Value (Json Str)
with expiry timer
´RTBRICK-MIBs
´RTBRICK-MIBs
Key/Value (Json Str.)
with expiry timer
periodic scans
Scans for JSONs
K/V for update
requests
Periodic Scans for
Update Requests

## Slide 5
Redis key structure
Key/Value
setting
Key/Value setting
periodic scans
Redis key is deleted after processing
Scans for JSONs
K/V setting
Periodic Scans for
bdsTableRequests
Key: bdsTableRequests-<requesterIP>-<#nr>
Value: bdsRequestInfo as JSON String
expiryTimer set to 60 secs
Key: bdsTableInfo-<rtbHostIp>-<rtbContName>-<rtbProcess>-<#nr>
Value: bdsTableInformation as JSON String
expiryTimer subject to table info
Key: bdsLoggingInfo-<rtbHostIp>-<rtbContName>-<#nr>
Value: logging infromation as JSON String
expiryTimer set to 60 secs
If scan does not return results
bdsRequest
Scans initated by get / getnext
K/V setting
Key: oidMibList-<oid>
Value: TBD
Key: oidMibLock-<oid>
Value: lock/unlock as JSON String
Key: oidMibNext-<oid>
Value: next-Oid-String
...
Key: oidRoot
Value: next-Oid-String

## Slide 6: RtBrick Test-Setup –Mac Air
Mac-Book Air, i5, 8GRAM, OSX 10.11.5
OSX 10.11.5
Kernel Darwin
VirtualBox 5.1
vIOS-XR
Gi 0/0/0/0:.31
vMX
ge-0/0/1.0: .11
RtBrick VM Ubuntu 16.4
enp0s9: .22
IPv4 Internet
vboxnet1 192.168.122.0/24
NAT
enp0s3: DHCP
Lxc RtBrick
vboxnet1: .1
Ansible &
Python Provisioning and Testing Tools
HTTP RPC client
(to RtBrick)
Provsioning client (via SSH to vMX and vIOS-XR)
en0: .DHCP
git
DSL/Mobile
CPE
vboxnet0: .1
enp0s8: .22
vboxnet0 192.168.56.0/24
http/ssh/snmp
ifp-0/1/1
10.0.3.50
bdsSnmpAdaptor

## Slide 7
Challanges:
BDS has not be designed for providing standard SNMP management information. There will be many constrains to gather data for even basic MIBs
  E.g. interface statistics for logical interfaces
SNMP has been development for over 30 years and has countless MIB elements
  Even if we try, we will not manage to implement basic sets of MIBs
   we must pursue a different approach
    implement standard MIBs only per customer use-case based
    Mirror BDS tables to SNMP OID tables
oidDict could hold Millions of entries, which would not scale in python datastructures anymore. Different approaches (e.g. BDS ) should be pursued

## Slide 8
RtBrick Enterprise MIBs
PEN has been assigned: 50058
High-Level concept for Rtbrick enterpise MIBs requires substantial effort.
  Once the OID tree has been defined, it will be hard to change
Transposing of BDS Table Schemas to SNMP Table Schemas could be done via scripts, if we have existing BDS Schema info
For prototyping, I used following mappings.
OID MIB bds table
50058 RTBRICK-MIB
50058.1 RTBRICK.bdstables
50058.1.1 RTBRICK-SYS-SW-INFO-TABLE-MIB local.system.software.info.confd
50058.1.2 RTBRICK-HOSTNAME-TABLE-MIB global.rtbrick.hostname.config
50058.1.3 RTBRICK-SYS-SW-INFO-TABLE-MIB global.confd.startup.status

## Slide 9
RtBrick Enterprise MIB Example
RTBRICK-SYS-SW-INFO-TABLE-MIB DEFINITIONS ::= BEGIN
--
-- Top-level infrastructure of the RtBrick enterprise MIB tree
--
IMPORTS
MODULE-IDENTITY, OBJECT-TYPE,
Integer32, enterprises FROM SNMPv2-SMI
TEXTUAL-CONVENTION, DisplayString,
PhysAddress, TruthValue, RowStatus,
TimeStamp, AutonomousType, TestAndIncr FROM SNMPv2-TC
bdsTables FROM RTBRICK-MIB;
systemSoftwareInfo MODULE-IDENTITY
LAST-UPDATED "201804140000Z"
ORGANIZATION "RtBrick"
CONTACT-INFO "E-mail: Stefan Lieberth <stefan@rtbrick.com>"
DESCRIPTION
"system_software_info"
REVISION "201804140000Z"
DESCRIPTION "Initial revision"
::= { bdsTables 1 }
--
-- rtbrick enterprise-specific management objects
--
systemSoftwareInfoTable OBJECT-TYPE
SYNTAX SEQUENCE OF SystemSoftwareInfoEntry
MAX-ACCESS not-accessible
STATUS current
DESCRIPTION
"A table of sw modue information"
::= { systemSoftwareInfo }
systemSoftwareInfoEntry OBJECT-TYPE
SYNTAX SystemSoftwareInfoEntry
MAX-ACCESS not-accessible
STATUS current
DESCRIPTION
"A row describing Rtbrick SW module information"
INDEX { name }
::= { systemSoftwareInfoTable 1 }
name OBJECT-TYPE
SYNTAX DisplayString (SIZE (0..255))
MAX-ACCESS read-only
STATUS current
DESCRIPTION
"attribute: library (1)"
::= { systemSoftwareInfoEntry 1 }
commitId OBJECT-TYPE
SYNTAX DisplayString (SIZE (0..255))
MAX-ACCESS read-only
STATUS current
DESCRIPTION
"attribute: commit_id (2)"
::= { systemSoftwareInfoEntry 2 }
commitDate OBJECT-TYPE
SYNTAX DisplayString (SIZE (0..255))
MAX-ACCESS read-only
STATUS current
DESCRIPTION
"attribute: commit_date (3)"
::= { systemSoftwareInfoEntry 3 }
packageDate OBJECT-TYPE
SYNTAX DisplayString (SIZE (0..255))
MAX-ACCESS read-only
STATUS current
DESCRIPTION
"attribute: package_date (4)"
::= { systemSoftwareInfoEntry 4 }
vcCheckout OBJECT-TYPE
SYNTAX DisplayString (SIZE (0..255))
MAX-ACCESS read-only
STATUS current
DESCRIPTION
"attribute: vc_checkout (5)"
::= { systemSoftwareInfoEntry 5 }
branch OBJECT-TYPE
SYNTAX DisplayString (SIZE (0..255))
MAX-ACCESS read-only
STATUS current
DESCRIPTION
"attribute: branch (6)"
::= { systemSoftwareInfoEntry 6 }
version OBJECT-TYPE
SYNTAX DisplayString (SIZE (0..255))
MAX-ACCESS read-only
STATUS current
DESCRIPTION
"attribute: version (7)"
::= { systemSoftwareInfoEntry 7 }
sourcePath OBJECT-TYPE
SYNTAX DisplayString (SIZE (0..255))
MAX-ACCESS read-only
STATUS current
DESCRIPTION
"attribute: source_path (8)"
::= { systemSoftwareInfoEntry 8 }
END

## Slide 10
BDS to OID transposing Example
def localSystemSoftwareInfoConfd(self,myOidDb,bdsAccessDict):
self.bdsTable = {'bdsRequest': {'process': 'confd', 'urlSuffix': '/bds/table/walk', 'table': 'local.system.software.info.confd'}}
bdsSuccess,responseJSON = bdsAccess.getJson(self.bdsTable,bdsAccessDict)
if bdsSuccess:
for ifObject in responseJSON["objects"]:
indexString = ifObject["attribute"]["library"]
indexCharList = [str(ord(c)) for c in indexString]
index = str(len(indexCharList)) + "." + ".".join(indexCharList)
myOidDb.insertOid(oidDbItem(oid = "1.3.6.1.4.1.50058.1.1.1.1.{}".format(index),
name = "name",
pysnmpBaseType = "OctetString",
fixedValue = indexString ) )
myOidDb.insertOid(oidDbItem(oid = "1.3.6.1.4.1.50058.1.1.1.2.{}".format(index),
name = "commitId",
pysnmpBaseType = "OctetString",
fixedValue = ifObject["attribute"]["commit_id"] ) )
myOidDb.insertOid(oidDbItem(oid = "1.3.6.1.4.1.50058.1.1.1.3.{}".format(index),
name = "commitDate",
pysnmpBaseType = "OctetString",
fixedValue = ifObject["attribute"]["commit_date"] ) )
myOidDb.insertOid(oidDbItem(oid = "1.3.6.1.4.1.50058.1.1.1.4.{}".format(index),
name = "packageDate",
pysnmpBaseType = "OctetString",
fixedValue = ifObject["attribute"]["package_date"] ) )
myOidDb.insertOid(oidDbItem(oid = "1.3.6.1.4.1.50058.1.1.1.5.{}".format(index),
name = "vcCheckout",
pysnmpBaseType = "OctetString",
fixedValue = ifObject["attribute"]["vc_checkout"] ) )
myOidDb.insertOid(oidDbItem(oid = "1.3.6.1.4.1.50058.1.1.1.6.{}".format(index),
name = "branch",
pysnmpBaseType = "OctetString",
fixedValue = ifObject["attribute"]["branch"] ) )
myOidDb.insertOid(oidDbItem(oid = "1.3.6.1.4.1.50058.1.1.1.7.{}".format(index),
name = "libraryVersion",
pysnmpBaseType = "OctetString",
fixedValue = ifObject["attribute"]["version"] ) )
myOidDb.insertOid(oidDbItem(oid = "1.3.6.1.4.1.50058.1.1.1.8.{}".format(index),
name = "sourcePath",
pysnmpBaseType = "OctetString",
fixedValue = ifObject["attribute"]["source_path"] ) )

## Slide 11
SNMP walk Example.
stefans-Air-3:~ slieberth$ snmpwalk -v 2c -c public -m All 192.168.56.22 1.3.6
RTBRICK-SYS-SW-INFO-TABLE-MIB::name."bd" = STRING: bd
RTBRICK-SYS-SW-INFO-TABLE-MIB::name."lwip" = STRING: lwip
RTBRICK-SYS-SW-INFO-TABLE-MIB::name."libqb" = STRING: libqb
RTBRICK-SYS-SW-INFO-TABLE-MIB::name."libbds" = STRING: libbds
RTBRICK-SYS-SW-INFO-TABLE-MIB::name."libbgp" = STRING: libbgp
RTBRICK-SYS-SW-INFO-TABLE-MIB::name."libldp" = STRING: libldp
RTBRICK-SYS-SW-INFO-TABLE-MIB::name."libspf" = STRING: libspf
RTBRICK-SYS-SW-INFO-TABLE-MIB::name."libdict" = STRING: libdict
RTBRICK-SYS-SW-INFO-TABLE-MIB::name."libfwdd" = STRING: libfwdd
RTBRICK-SYS-SW-INFO-TABLE-MIB::name."libisis" = STRING: libisis
RTBRICK-SYS-SW-INFO-TABLE-MIB::name."libconfd" = STRING: libconfd
RTBRICK-SYS-SW-INFO-TABLE-MIB::name."libtiger" = STRING: libtiger
RTBRICK-SYS-SW-INFO-TABLE-MIB::name."rtbshark" = STRING: rtbshark
RTBRICK-SYS-SW-INFO-TABLE-MIB::name."json_parser" = STRING: json_parser
RTBRICK-SYS-SW-INFO-TABLE-MIB::name."librtbutils" = STRING: librtbutils
RTBRICK-SYS-SW-INFO-TABLE-MIB::name."libproto_infra" = STRING: libproto_infra
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitId."bd" = STRING: 3d298f2d7c52c94d78620a16e444ef28d04f2815
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitId."lwip" = STRING: e47c8befcc6f2caa64e9ac1a32bfb0d6c1b6ec4d
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitId."libqb" = STRING: 6bc9a2b7901fe4a1fd91d571f4bfd5640e32c985
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitId."libbds" = STRING: 90e29a27bb15df75719b62636277b12c151e3573
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitId."libbgp" = STRING: 3f5c9fdcaa00abeb83371876aebae11bf6814fff
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitId."libldp" = STRING: 49d7575942aa3363023903ecd5a0c6138537c0bd
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitId."libspf" = STRING: 68fb6ee310afdd4285e8ecb5a9d180232e13bb75
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitId."libdict" = STRING: 4d2d5393d9ad77749342265d63639705b1c8a3b1
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitId."libfwdd" = STRING: 6b07b093c6a0f1b54dcd9f0f6fd8892a55c109e8
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitId."libisis" = STRING: a5996e83f0ab5d223ec879507290b0c73c93369e
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitId."libconfd" = STRING: 30757439755223c02caa79ea1708cde773eac9a9
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitId."libtiger" = STRING: 97b1c21552537286cfa945637f70b259dc609c3f
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitId."rtbshark" = STRING: e39fef1fa9344a8ce335970a48a02bbb880c180d
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitId."json_parser" = STRING: 94656913a98cea1b427e6b9ae6c744e27530d45b
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitId."librtbutils" = STRING: 41e2141b93f28ce2d9c86b7e74d701eaa96c78e4
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitId."libproto_infra" = STRING: 80f3e6d1f7d826abea9f03c954d9f9cc3b743fa1
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitDate."bd" = STRING: Fri Jun 8 10:23:54 2018 +0530
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitDate."lwip" = STRING: Tue Jun 12 10:15:36 2018 +0530
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitDate."libqb" = STRING: Sun Apr 1 20:38:29 2018 +0530
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitDate."libbds" = STRING: Tue Jun 12 12:20:37 2018 +0530
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitDate."libbgp" = STRING: Fri Jun 8 15:04:46 2018 +0530
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitDate."libldp" = STRING: Sat May 12 15:36:33 2018 +0530
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitDate."libspf" = STRING: Fri Mar 30 00:46:28 2018 +0530
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitDate."libdict" = STRING: Fri Mar 30 02:43:56 2018 +0530
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitDate."libfwdd" = STRING: Wed Jun 13 01:01:55 2018 +0530
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitDate."libisis" = STRING: Wed Jun 13 14:23:23 2018 +0530
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitDate."libconfd" = STRING: Mon Apr 16 18:16:14 2018 +0530
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitDate."libtiger" = STRING: Tue Jun 13 10:38:52 2017 +0530
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitDate."rtbshark" = STRING: Wed Mar 21 20:56:13 2018 +0530
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitDate."json_parser" = STRING: Tue Jan 9 16:12:30 2018 +0530
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitDate."librtbutils" = STRING: Fri Jun 8 13:06:08 2018 +0530
RTBRICK-SYS-SW-INFO-TABLE-MIB::commitDate."libproto_infra" = STRING: Tue Jun 12 15:20:37 2018 +0530

## Slide 12
ubuntu@Tropos:~$ rtb bgp.appd.1 show backstore print-pretty-table C1_CRS.bgp.peer.config
object: 1, sequence: 1, last update: Sat Jul 14 06:50:55 2018
attribute: peer_ipv4_address (1), type: ipv4addr (12), length: 4, value: 49.100.1.1
attribute: source_ipv4_address (3), type: ipv4addr (12), length: 4, value: 49.100.1.2
attribute: peer_group_name (6), type: string (9), length: 13, value: C1_CRS_v4_PG
object: 2, sequence: 2, last update: Sat Jul 14 06:51:01 2018
attribute: peer_ipv6_address (2), type: ipv6addr (15), length: 16, value: 2003:4:f022:fd00::1
attribute: source_ipv6_address (4), type: ipv6addr (15), length: 16, value: 2003:4:f022:fd00::2
attribute: peer_group_name (6), type: string (9), length: 13, value: C1_CRS_v6_PG
Transposing of customized tables::
bgpPeerConfigEntry OBJECT-TYPE
SYNTAX SystemSoftwareInfoEntry
MAX-ACCESS not-accessible
STATUS current
DESCRIPTION
"A row describing Rtbrick SW module information"
INDEX { instance, ipAddressType, peerAddress }
::= { systemSoftwareInfoTable 1 }
SystemSoftwareInfoEntry ::= SEQUENCE {
instance DisplayString,
ipAddressType integer,
peerAddress DisplayString,
sourceAddress DisplayString,
peerGroupName DisplayString,
}
RTBRICK-BGP-PEER-CONFIG-MIB::instance.”C1_CRS”.4.”49.100.1.1” = STRING: C1_CRS
RTBRICK-BGP-PEER-CONFIG-MIB::ipAddressType.”C1_CRS”.4.”49.100.1.1” = INTEGER: 4
RTBRICK-BGP-PEER-CONFIG-MIB::peerAddress.”C1_CRS”.4.”49.100.1.1” = STRING: ”49.100.1.1”
RTBRICK-BGP-PEER-CONFIG-MIB::sourceAddress.”C1_CRS”.4.”49.100.1.1” = STRING: ”49.100.1.2”
RTBRICK-BGP-PEER-CONFIG-MIB::peerGroupName.”C1_CRS”.4.”49.100.1.1” = STRING: ”C1_CRS_v4_PG”
RTBRICK-BGP-PEER-CONFIG-MIB::instance.”C1_CRS”.6.”2003:4:f022:fd00::1” = STRING: C1_CRS
RTBRICK-BGP-PEER-CONFIG-MIB::ipAddressType.”C1_CRS”.6.”2003:4:f022:fd00::1” = INTEGER: 6
RTBRICK-BGP-PEER-CONFIG-MIB::peerAddress.”C1_CRS”.6.”2003:4:f022:fd00::1” = STRING: ”2003:4:f022:fd00::1”
RTBRICK-BGP-PEER-CONFIG-MIB::sourceAddress.”C1_CRS”.6.”2003:4:f022:fd00::1” = STRING: ”2003:4:f022:fd00::2”
RTBRICK-BGP-PEER-CONFIG-MIB::peerGroupName.”C1_CRS”.6.”2003:4:f022:fd00::1” = STRING: ”C1_CRS_v6_PG”
Automated transposing form BDS schema to MIB is not possible, as there are ambiguous indices in BDS:
peer_ipv4_address
peer_ipv6_address
BDS table
MIB draft
SNMP GET (expected - draft)